## Slide 1
GUC Masters · Smart City Capstone · 2026
SMART CITY CAPSTONE · GUC MASTERS
Categorize-then-Predict Trustworthy PM2.5 where there is no sensor — and a few days ahead
Kampala, Uganda · 39 low-cost sensors · free data only
The question Can a categorize-then-predict pipeline give an urban planner trustworthy PM2.5 where there is no sensor, and a few days ahead, without collapsing? This deck reports the honest answer — out-of-site and out-of-time, negative results included.

## Slide 2
GUC Masters · Smart City Capstone · 2026
01 · RESEARCH JOURNEY
From 60+ Papers Down to 4
60+ screened Air-quality + ML + remote-sensing literature for low-resource cities.
4 anchors kept Each builds on the last — precedent, levers, honest evaluation.
1 gap Models look great on a random split, then collapse at a new place.
→ The gap — generalization to unseen places — is exactly what the 4th cap attacks.

## Slide 3
GUC Masters · Smart City Capstone · 2026
02 · THE FOUR PAPERS
Each Paper Builds on the Last
Adong 2025 Kampala PM2.5 from satellite AOD alone — weather deliberately excluded. Our precedent.
Weather lever ERA5 weather is the cheap, generalizable signal the precedent left out.
Honest evaluation African spatial-CV ~0.13 vs random >0.90 — collapse is the norm, not the exception.
Land-use regression Road density / distance-to-road / terrain transfer to new locations.
→ Together: cheap data can work — but only if evaluated honestly and given place-structure.

## Slide 4
GUC Masters · Smart City Capstone · 2026
03 · THE REFRAME
From “Which Lever?” to “Categorize-then-Predict”
Old framing (3rd cap) “Which cheap data lever helps estimate PM2.5?” → a finding (weather helps, LST is inert), but the tool collapses at a sensor-less place.
New framing (4th cap) A clinic, not one doctor: a triage nurse sorts each place into a kind, then the specialist for that kind predicts.
Two metrics — kept separate end to end:
NOW · nowcast PM2.5 today at a sensor-less place. Honest test = leave-sites-out. Bar = the blind pooled model.
FUTURE · forecast PM2.5 +1…7 days at a known place. Honest test = chronological. Bar = persistence (“same as yesterday”).
→ Different question, different honest test, different bar, different best model.

## Slide 5
GUC Masters · Smart City Capstone · 2026
04 · THE DATA
39 Sensors · One Merged Table · Free Inputs Only
39
AirQo sensors
13,944
site-days
~84%
daily coverage
38
µg/m³ mean PM2.5
Predictors (free, available anywhere) ERA5 weather (temp · dew-point · wind · pressure · rain) + location + calendar. LST carried but proven inert.
Banned as predictors pm10 (same instrument as the target, corr ≈ 0.9) and n_obs (a by-product of the daily mean) — neither exists at a sensor-less place, so using them would manufacture a fake win.
→ Honest features first: nothing a planner could not actually obtain at a new address.

## Slide 6
GUC Masters · Smart City Capstone · 2026
05 · THE COLLAPSE
Looks Great — Until You Point It Somewhere New
0.81
leaky random-split R²
0.31
honest new-site R²
~0
one new-site fold
Why it matters The headline R²≈0.81 is a leaky random split — it tests on the same sensors it trained on (gap-filling). Graded honestly (hide whole sensors, or forecast the real future) it collapses, and a “same-as-yesterday” guess beats it out-of-time. A planner needs PM2.5 where there is no sensor.
→ The whole 4th cap exists to stop this collapse — without faking the test.

## Slide 7
GUC Masters · Smart City Capstone · 2026
06 · CATEGORIZE (CP-A)
39 Sensors → 3 Behavioural Kinds of Place
24
low-pollution / well-ventilated — the city baseline
PM2.5 ≈ 31.7
12
high-pollution / well-ventilated — hotter spots, still windy
PM2.5 ≈ 47.5
3
moderate / stagnant — low wind + humid, a robust micro-regime
PM2.5 ≈ 46.5
Robust + portable Same 3 stagnant sites at every k; k-means agrees with Ward. Categories are spatially intermixed — they capture behaviour, not geography. A new site is categorized from its signature, snapped to the nearest centroid.
→ Kampala is homogeneous in level; the structure is low-vs-high pollution + 3 stagnant outliers.

## Slide 8
GUC Masters · Smart City Capstone · 2026
07 · THE HONEST LADDER (CP-B)
Knowing the Category Beats the Blind Model
New-site R² (leave-sites-out) — climb only if the rung below holds:
blind (no category)
0.316
+ category · k=4 (tuned)
0.558
+ category + geodata · k=4
0.564
Significant Tuning categories to k=4 (by honest R², not silhouette) lifts the deploy-only nowcast 0.48→0.56. Paired bootstrap +1.07 µg/m³, CI [+0.33, +1.90].
Soft routing wins Category-as-a-feature tolerates a wrong category; mixture-of-experts hard-routes and collapses (0.50→0.30) under realistic cold-start.
→ Ceiling: leave a whole category out → negative. Interpolates among known kinds, can’t extrapolate.

## Slide 9
GUC Masters · Smart City Capstone · 2026
08 · NOW BAKE-OFF (CP-D)
The Model Is Not the Bottleneck
New-site R² · same +category features · four learners:
0.529
RandomForest
0.482
XGBoost
0.469
LightGBM
0.465
CatBoost
Best: RandomForest Lowest leaky score yet highest new-site score — it overfits least, transfers best. But all 4 cluster (0.47–0.53).
Conformal — fixed Calibrating on held-out SITES (group conformal) lifts new-site 90%-interval coverage 74.8% → 85.8%. Bands widen honestly.
→ The category feature (+0.16) moved R² far more than any model swap. Features > learner.

## Slide 10
GUC Masters · Smart City Capstone · 2026
09 · BREAK THE CEILING
Free Map Data Nowcasts a Sensor-less Site
0.32
blind
0.42
+ geodata · ZERO sensors
0.55
+ category + geodata
Land-use regression, sourced free OSM road density + distance-to-nearest-major-road (Overpass, 43,870 ways) + SRTM elevation. Static, need ZERO pollution observations. dist-to-major-road is the clearest signal (closer → higher PM2.5).
A complement, not a substitute Geodata can’t name the category (54% < 62% baseline) — it adds independent signal. Combined is best, and most stable (±0.046).
→ The bridge from “a finding” to “a tool a planner can point at any address.”

## Slide 11
GUC Masters · Smart City Capstone · 2026
10 · FORECAST (CP-D)
A Real Forecaster Holds R²≈0.43 a Week Out
R² by horizon (chronological, out-of-time):
horizon
persistence
GBM-on-lags
LSTM
+1 day
0.34
0.43
0.51
+3 days
0.11
0.37
0.48
+7 days
0.02
0.33
0.43
LSTM earns its weight Global LSTM + category embedding beats the GBMs at every horizon (+0.04…+0.12), lead widening with horizon. All beat persistence. Correction: forecasting does NOT decay to ~0 by +7d.
→ Persistence-beats-model was true only for the nowcast model — not a purpose-built forecaster.

## Slide 12
GUC Masters · Smart City Capstone · 2026
11 · SAFETY TIERS
From a Number to a Safety Status
EPA PM2.5 safety bands — what a city official actually needs:
Elevated
≤ 35.4 µg/m³
High
35.5 – 55.4
Dangerous
> 55.4
Graded by the BAND it lands in — same honest tests:
New-site (no sensor) Exact tier 68% · within one tier 98.5% · vs 52% majority baseline. A 2-tier error (a Dangerous area called safe) for only 3.6% of days.
Forecast +1→+7d Exact tier 70% → 68% · within one tier ~98% · beats the persistence-band baseline at every horizon.
→ R² punished 47-vs-52 misses; in safety tiers those are the SAME band — so the tool is deployable.

## Slide 13
GUC Masters · Smart City Capstone · 2026
12 · DANGER ALERTING
Catching the Days That Matter — a Planner's Dial
Lower the Dangerous alert cutoff → catch more dangerous days, at a chosen false-alarm cost (honest new-site):
alert if predicted >
dangerous-day recall
false-alarm rate
55.4 (strict EPA)
0.51
4%
50
0.67
8%
45 (suggested)
0.80
17%
40
0.91
30%
Why it works Dangerous days are a humid, stagnant weather regime (humidity + dew-point separate them most) — the model keys on weather to flag them.
Honest negative A dedicated class-weighted detector did NOT beat simply lowering the regressor's threshold. The simpler lever wins.
→ The planner owns the operating point: 80% of dangerous days caught at a 45 µg/m³ alert cutoff.

## Slide 14
GUC Masters · Smart City Capstone · 2026
13 · THE VERDICT
The Reframe Works — With Honest Limits
What worked Category lifts new-site R² 0.32→0.48 (significant). Free geodata: 0.42 zero-deploy, 0.55 combined. LSTM holds 0.43 at +7d.
What didn’t Mixture-of-experts collapses under cold-start. Category×month prior hurts under noise. Geodata can’t name the category.
Bounded Leave-a-whole-category-out goes negative — can interpolate among known kinds, can’t extrapolate to an unseen regime.
Two prior claims corrected (verified) 1) Forecasting does not decay to ~0 by +7d — an artefact of using a nowcast model to forecast. 2) “Categorization can’t rescue a homogeneous city” is too pessimistic — it lifts new-site R² by +0.16; true only for unseen regimes.
→ Honesty over headlines — every win holds out-of-site and out-of-time, or it isn’t reported.

## Slide 15
GUC Masters · Smart City Capstone · 2026
14 · CONTRIBUTION & NEXT
A Cheap, Honest PM2.5 Safety Tool for a Low-Resource City
The contribution Free data + behavioural categories + land-use geodata turn a collapsing model into a deployable safety-triage tool: classify a never-instrumented area's safety tier (68% exact / 98.5% within one tier) and forecast a week ahead — evaluated the way a planner will actually use it.
Done · safety tiers band evaluation + planner-tunable danger alerting (80% recall)
Done · sharper model k=4 categories (0.56) + group conformal (86% coverage)
Next · more places 39 sites is small — more sensors/categories sharpen routing
Next · push recall cost curves to 90% danger recall · tighter conformal to 90%
→ Reproducible: fixed seeds · honest splits · scripts + result CSVs in 4th-cap-handover/analysis/.